## Slide 1
NOV 2021
Safyzan Salim
scriptworkz ent
MQTT on Pi

## Slide 2
MQTT on Pi – Let’s Start
Scenario
SZS - Nov 2021
You have been assigned to monitor the temperature and moisture of a server room. The results can be monitored anywhere. Your system must be able to capture 2 server racks’ temperature and humidity, and also the server room’s temperature and humidity too.
Future Project >>A notification alarm will be activated if the any of the sensors passes the certain condition, e.g., rack temperature greater than 25°C, or server room’s temp too high… etc.

## Slide 3
MQTT on Pi – Let’s Start
Prerequisites
https://mqtt.org
SZS - Oct 2021
Hardware:
Raspberry Pi board with:
  -Raspberry Pi OS
  -16 GB class 10 microSD
  -5V 2.5A power supply
ESP32 with Temperature & Humidity Sensor, DHT11**
Software:
Node-RED
Arduino IDE
Arduino Client for MQTT library
Aedes MQTT
WiFi:
A 2.4G AP
** This project uses Grove - Temperature & Humidity Sensor (DHT11)

## Slide 4
MQTT on Pi – Let’s Start
How It Works
SZS - Nov 2021
ESP32 & DHT11 will be fixed at a rack, named Rack#1 at Lab A. Aedes broker is running on a Raspberry Pi (PC/Laptop/Mac).
After connected to WiFi, data from ESP32 will be sent to broker.
Since the Node-RED has subscribed topic labA/rack1/temp & labA/rack1/humid from ESP32, both information (temp & humid) will be displayed at debug & also gauges – in real time.
Raspberry Pi / Laptop / Desktop – Cross Platform

## Slide 5
SZS - Oct 2021
MQTT on Pi – Let’s Start
i. Install & Run Aedes Broker Service
Node-RED Menu > Manage palette > Install > type aedes at search module > node-red-contrib-aedes > install
Wait & make sure the install button changed to installed.
Type aedes
Click install
Execute Node-RED service.
Install Aedes broker by clicking:

## Slide 6
SZS - Nov 2021
MQTT on Pi – Let’s Start
ii. Test Aedes Broker Service
* Please check your device IP address.
** Do not use 1880 – reserved to localhost:1880
Setup as in the figure.
Configurations:
  BROKER IP = 192.168.0.108*
  MQTT port = 1990 **
  Topic = demo/welcome
Download: https://bit.ly/3olPfcE

## Slide 7
SZS - Nov 2021
MQTT on Pi – Let’s Start
iii. Deploying Aedes Broker
Configurations:
  Broker IP = 192.168.0.108*
  MQTT port = 1889**
  MQTT_IN = labA/rack1/temp  node#1
  MQTT_IN = labA/rack1/humid  node#2
Download palette: https://bit.ly/3qGwyTE.
* Please check your device IP address.
** do not use 1880 – reserved to localhost:1880
node#1
node#2

## Slide 8
SZS - Nov 2021
MQTT on Pi – Let’s Start
iv. Arduino Client MQTT
Sketch > Include Library > Manage Libraries
Install New Library by opening Library Manager and search for PubSubClient by Nick O’Leary – latest version.
PubSubClient
Nick O’Leary

## Slide 9
SZS - Nov 2021
MQTT on Pi – Let’s Start
Download the file working file from https://bit.ly/30dwDnb.
v. Arduino PubSub Sketch
Remove // and put // at Line#15 if you are using NodeMCU.
Place a jumper at signal pin to pin 26 of ESP32.
#16
#24
#17

## Slide 10
SZS - Nov 2021
MQTT on Pi – Let’s Start
v. Arduino PubSub Sketch
IP address of your Node-RED device.
Set your SSID & password.
Download the file working file from https://bit.ly/30dwDnb.
#34
#32
#33

## Slide 11
SZS - Nov 2021
MQTT on Pi – Let’s Start
v. Arduino PubSub Sketch
#50
#59
#57
#53
#52
Download the file working file from https://bit.ly/30dwDnb.
Reading from DHT11 sensor
From Serial Monitor

## Slide 12
SZS - Nov 2021
MQTT on Pi – Let’s Start
Download the file working file from https://bit.ly/30dwDnb.
v. Arduino PubSub Sketch
A function to connect the ESP32 / NodeMCU to existing access point (WiFi).
Check your SSID & password in case non-stop dotted line appears.

## Slide 13
SZS - Nov 2021
MQTT on Pi – Let’s Start
Download the file working file from https://bit.ly/30dwDnb.
v. Arduino PubSub Sketch
ESP32 @ NodeMCU ensure persistent connection between MCU and the broker.

## Slide 14
SZS - Nov 2021
MQTT on Pi – Let’s Start
Download the file working file from https://bit.ly/30dwDnb.
v. Arduino PubSub Sketch
Set 2 array elements; temp_hum_val[0] & temp_hum_val[1]. Set both value = 0.
Start to read temp & humid from sensor.
Print both values; temp & humid at Serial Monitor.
Convert temp & humid from float to char.
Publish the temp & humid value accordingly. Topic name must match with Node-RED’s topic.
Will reconnect to broker if disconnected.
L#127
L#124
L#125
L#136
L#127
L#133

## Slide 15
SZS - Nov 2021
MQTT on Pi – Let’s Start
Node-RED Debug Window
v. Arduino PubSub Sketch – Expected Output
Arduino’s Serial Monitor
* Do check your IP address, Topic at your sketch if you did not get as expected
output.

## Slide 16
SZS - Nov 2021
MQTT on Pi – Let’s Start
vi. Create Visual Dashboard
Node-RED Menu > Manage palette > Install > type dashboard at search module > node-red-dashboard > install
Go to Node-RED editor.
Install Dashboard broker by clicking:

## Slide 17
SZS - Nov 2021
MQTT on Pi – Let’s Start
vi. Create Visual Dashboard
In order to run a Node-RED dashboard, you need to create a tab &
a group.
Decide what information that you want to display.
In our case, you should consider:
  Classroom : Lab A
  Rack ID: 1
  Item to visual/display: Temperature & Humidity
Thus,
  Tab = Main Title = Lab A
  Group = Sub Title = Rack1
FYI, more than 1 group can be hosted by 1 tab.
Your tab can also host group from other tab.

## Slide 18
SZS - Nov 2021
MQTT on Pi – Let’s Start
vi. Create Visual Dashboard
S2
We need to setup dashboard properties before connecting the gauge/meter node to the flow.
Step 1: Click the dropdown Menu of Node-RED.
Step 2: Click Dashboard link.
S1

## Slide 19
SZS - Nov 2021
MQTT on Pi – Let’s Start
vi. Create Visual Dashboard
Step 3: Create a project by clicking .
Step 4: Add element in your project by clicking at .
You may edit/update/delete tab properties or group properties by clicking at .
S3
S4

## Slide 20
SZS - Nov 2021
MQTT on Pi – Let’s Start
vi. Create Visual Dashboard
Step 5: Click to edit the Tab 1 name .
Step 6: Change Tab 1 with Lab A.
Step 7: Next, click to save the setting.
S5
Step 4
S6
S7

## Slide 21
SZS - Nov 2021
MQTT on Pi – Let’s Start
vi. Create Visual Dashboard
Step 8: Click edit tab at Group 1.
Step 9: Change Group 1 to Rack 1.
Step 10: Click Update tab to save the setting..
S8
S9
S10

## Slide 22
SZS - Nov 2021
MQTT on Pi – Let’s Start
vi. Create Visual Dashboard
Step 11: Now, add 2 gauges from dashboard palette.
Step 12: Wire each gauge to labA/rack1/temp & labA/rack1/humid respectively.
Any of dashboard palette must be configured into its specific tab & group.
The chances of your node appears in different tab will happen when you mistakenly mapped the groups & tabs.
S11
S12

## Slide 23
SZS - Nov 2021
MQTT on Pi – Let’s Start
vi. Create Visual Dashboard
Configuration of Gauges.
Step 13: Double click gauge connected to labA/rack1/temp.
Step 19: Double click gauge connected to labA/rack1/humid.
**Item to change.
S19
**
**
**
**
S13

## Slide 24
SZS - Nov 2021
MQTT on Pi – Let’s Start
vi. Create Visual Dashboard
Update Temperature Gauge Properties.
Step 14: Click textbox at . Change [unassigned] Group 1
to select [Lab A] Rack 1.
Step 15: Change text gauge to Temperature at .
Step 16: Replace units with ° C (you may copy ° here).
Step 17: Replace maximum range 10 with 50
DHT11’s range is between 0° C to 50° C.
Step 18: Click upon completion. **Item to change.
S14
S15
S16
S17
S18

## Slide 25
SZS - Nov 2021
MQTT on Pi – Let’s Start
vi. Create Visual Dashboard
Update Humidity Gauge Properties.
Step 20: Click textbox at . Change [unassigned] Group 1
to select [Lab A] Rack 1.
Step 21: Change text gauge to Temperature at .
Step 22: Replace units with ° C (you may copy ° here).
Step 23: Replace maximum range 10 with 50
Humidity range is between 0° C to 100° C.
Step 24: Click upon completion.
Step 25: Node-RED offers a few interactive visual for metering.
You may go to Type & select the output that suit with your needs.
Do not forget to click Deploy button.
S20
S21
S22
S23
S24
S25

## Slide 26
SZS - Nov 2021
MQTT on Pi – Let’s Start
vi. Create Visual Dashboard
Node-RED Dashboard
Node-RED Flow Editor
Download the file working file from https://bit.ly/3DfNfsI.

## Slide 27
SZS - Nov 2021
MQTT on Pi – Let’s Start
vi. Create Visual Dashboard
Adding More Racks.
In order to add more rack, means you have to add more sensors.
You have to consider the topic at ESP32 and also at broker side.
Assume you want to add Rack 2, Lab A. Open arduino sketch (https://bit.ly/31WQUhn) and change:
  labA/rack1/humid at line number 133 to labA/rack2/humid, and also ,
  labA/rack1/temp at line number 134 to labA/rack2/temp.
Next, at Node-RED flow editor, add 2 mqtt in, set IP address similar with steps, label the topic as labA/rack2/humid and labA/rack2/temp.

## Slide 28
QUESTIONS
END
SZS - Oct 2021